Air Operated Vacuum Cleaners

55 Gallon Series Model Specific Features: Model 1J55 Tank Size 55 gallon Suction CFM 145 CFM Static Lift H20/ Hg 180” H20/ 13”HG Input PSI 90PSI Input CFM 40 CFM Wet / Dry Recovery Yes Tank Material Painted Steel Weight 140lbs.

55 Gallon Air Operated Vacuum

Our 55 Gallon wet/dry air operated vacuum cleaner is the ideal unit for tough clean up jobs. With no moving parts you can run the machine continuously. These units are non-electric and ideal for hazardous dust !! Filter systems are grounded assuring you of spark free operation. Air Operated Series Common Features: 2-Stage filter system efficient to 1 Micron Oversized wheels and casters for increased mobility 55 Gallon Painted Steel Tank Quite Operation under 80 DBA Washable “Tetra-Tec main filter 2 Tank set-up (see picture below) Grounded Hose & Cleaning tools Unit shipped with 3 different air jet sizes PSI Gauge standard on all units Incredibly easy to replacement muffler insert Optional Features: 55 Gallon drum transfer lids for additional capacity ULPA/HEPA Filters available Nomex Hi-Temp filters available Complete selection of 1¼” , 1½” and 2” attachments External Filter option Vacuum gauges & manometers are available AMERICAN VACUUM, 7301 N. MONTICELLO AVE, SKOKIE, IL 60076 TOLL FREE: 800-321-2849 FAX: 847-674-0214 www.americanvacuum.com Email: sales@americanvacuum.com

# Text boxes

American Vacuum Co.   Equipment Data Sheet

American Vacuum Company        Equipment Data Sheet

AMHose and Cleaning Tools   ●   Central Vacuum Tube and Fittings   ●   Custom Controls

AMERICAN VACUUM,  7301 N. MONTICELLO AVE,  SKOKIE, IL 60076

TOLL FREE: 800-321-2849    FAX: 847-674-0214

www.americanvacuum.com    Email: sales@americanvacuum.com